## Slide 1: CSE-671 Embedded Systems Term Project: The Garage Backup Alert System
Philip Geramian
Syracuse University College of Engineering and Computer Science
May 6, 2016

## Slide 2: Main Idea
Parking Car in garage at home
  Easy To pull into when arriving
  Hard to back into when leaving
Why not back in when arriving?
  Hard to tell how much space you have between you and the wall
  Would make leaving easier

## Slide 3: Architecture
BeagleBone Black
  Running Debian 7.9 3.8.x Linux Kernel
XL-MaxSonar Range Finder
315MHz Transmitter Receiver pair
  For the Remote
Arduino Pro Mini
Custom 7 – Segment Display
Custom Enclosure

## Slide 4: Techniques
Acquire distance from XL-MaxSonar Via UART
  Process and convert from cm to inches
If in our range display on screen
  Via SPI and bit manipulation
Send message to Remote
  If less than 36 send message 0
  If greater than 40 send message 1
  Via UART
On Boot setup devices and start monitoring program

## Slide 5: Peripherals
BeagleBone Black
  Embedded Linux System
XL-Max Sonar
  Sonic Range Finder that gives data via UART
315MHz Transmitter Receiver pair
  Accepts/ puts out raw data
  Can transmit a UART signal
Arduino Pro Mini
  Simple microcontroller to control remote

## Slide 6: Challenges
315 MHz Transmitter Receiver pair
  Have to encapsulate data due to noisy system
XL-MaxSonar
  Outputs inverted UART
  Advertised as 0->195 inches
  In testing 11->~90 inches
    Still usable for project
Custom Display
  Needs values stored together as a 1 byte binary value
    Ex: 27 needs to be 00100111
Housing
  Has to be able to fit everything, and have long enough wires to reach all components

## Slide 7: References
[1] - http://www.maxbotix.com/documents/XL-MaxSonar-WR_Datasheet.pdf
[2] - Exploring BeagleBone: Tools and Techniques for Building with Embedded Linux By Derek Molloy
[3] - https://www.arduino.cc/en/Reference/Serial
[4] – http://www.mpja.com/download/31960MPSch.pdf
[5] - http://www.jameco.com/Jameco/Products/ProdDS/13696.pdf
[6] – https://www.nxp.com/documents/data_sheet/74HC_HCT595.pdf
[7] - https://github.com/saterblader/Beaglebone/tree/master/LIBS